## Slide 1
DAY 2 OF 5
Foundations — Part 2 & Integration Begins
"Advanced Instruments & Multi-Instrument Introduction"
5-Day SDI Lab Automation FDP • v2.0
Mahaveer. Rajendra. Savanur
Head of Engineering & AI Systems
Spruha Build-in Solutions | Powered by Moku:Go — Liquid Instruments

## Slide 2
Day 2 Agenda
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
1
8:00 – 8:15
Day 1 Recap quick quiz + questions
2
8:15 – 10:30
AWG + Logic Analyzer live demos + Exercises 2.1 and 2.2
3
10:45 – 12:30
Day 1 Capstone: Frequency Response Tester team project
4
1:30 – 2:30
Capstone Presentations 5 min per team
5
2:45 – 5:00
Multi-Instrument Mode Fundamentals routing, demo, Exercise 2.3

## Slide 3
Day 1 Recap — What You've Mastered
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Oscilloscope
Frame capture, CSV logging,
Vpp statistics, summary plots
Waveform Generator
Parametric testing,
frequency sweeps, duty/symmetry
Automation Loops
21-test sequences, progress logs,
efficiency measurement
The Pattern
Connect → Configure →
Acquire → Cleanup
try/finally every time
Pop quiz: What does get_data() return? Why relinquish_ownership()? What happens without force_connect?

## Slide 4
Arbitrary Waveform Generator — Live Demo
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
day2/ex2_1_awg_custom_waveforms.py
from moku.instruments import ArbitraryWaveformGenerator
import numpy as np
awg = ArbitraryWaveformGenerator(MOKU_IP,
force_connect=True)
try:
# define ANY waveform mathematically
t = np.linspace(0, 1, 256, endpoint=False)
saw = 2*t - 1
stairs = np.floor(t*8)/4 - 1
for wf in (saw, stairs):
wf = wf / max(abs(wf)) # normalize [-1, 1]
awg.generate_waveform(
channel=1,
sample_rate='Auto',
lut_data=list(wf), # LIST, not ndarray
frequency=1e3,
amplitude=1.0)
time.sleep(2)
finally:
awg.relinquish_ownership()
Custom waveform library: sine, sawtooth, triangle, staircase, half-rectified sine
Key Concepts
lut_data rules
plain Python list — list(arr)
normalized to [-1, 1]
#1 mistake
passing a numpy array directly —
always wrap with list()
Why AWG?
sensor simulation, distortion,
anything math can define

## Slide 5
Exercise 2.1: Custom Waveform Library
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Objective: Create 5 custom waveforms with numpy, build a reusable JSON library, output each on the AWG
Requirements
✓
Build: sine, sawtooth, triangle,
✓
staircase, half-rectified sine (256 pts)
✓
Normalize every waveform to [-1, 1]
✓
Preview plot BEFORE hardware output
✓
Save library to waveform_library.json
✓
Output each at 1 kHz / 1 Vpp
Expected Output
Preview saved: waveform_library.png
Library saved: waveform_library.json
Generating: sine @ 1 kHz
Generating: sawtooth @ 1 kHz
Generating: staircase @ 1 kHz
All 5 waveforms output successfully.
Duration: 30 minutes
Bonus Challenge: Add a Gaussian pulse and a chirp; reload the JSON and replay it
Script: day2/ex2_1_awg_custom_waveforms.py • compare with expected_outputs/ex2_1_expected.png

## Slide 6
Logic Analyzer — Hardware-Verified API
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
day2/ex2_2_logic_analyzer_spi.py
from moku.instruments import LogicAnalyzer
la = LogicAnalyzer(MOKU_IP, force_connect=True)
try:
clock = [1, 0] * 50
mosi = [1,0,1,1,0,0,1,0] * 12 + [0]*4
# ALL pins in ONE call to PG channel 1
la.set_pattern_generator(
channel=1,
patterns=[
{"pin": 1, "pattern": clock[:100]},
{"pin": 4, "pattern": mosi[:100]},
],
divider=5)
# pin mode is 'PG1' — NOT 'Pattern'
la.set_pin_mode(1, 'PG1')
la.set_pin_mode(4, 'PG1')
data = la.get_data(include_pins=[1, 4])
finally:
la.relinquish_ownership()
Hardware-verified March 2026 on moku v4.1.2 / MokuOS 4.1.2
Key Concepts
Verified fixes
channel=1 is the PG channel,
NOT a pin number
patterns = list of dicts
Pin mode is 'PG1'
never 'Pattern' — that is the
old, broken API
Use it for
SPI / I2C / UART teaching,
protocol timing diagrams

## Slide 7
Exercise 2.2: SPI Bus Pattern Generation
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Objective: Generate a 4-pin SPI-like bus with the pattern generator and capture it back
Requirements
✓
Pin 1: CLK — square wave
✓
Pin 2: DATA — byte pattern
✓
Pin 3: CS — frame select
✓
Pin 4: MOSI — data out
✓
ONE set_pattern_generator call, 4 pins
✓
Capture with get_data(include_pins=[1,2,3,4])
Expected Output
Pin 1 (CLK): 100 samples
Pin 2 (DATA): 100 samples
Pin 3 (CS): 100 samples
Pin 4 (MOSI): 100 samples
Captured data from 4 pins.
Plot saved: spi_signals.png
Duration: 30 minutes
Bonus Challenge: Re-create a UART frame: start bit + 8 data bits + stop bit; add even parity
Script: day2/ex2_2_logic_analyzer_spi.py • compare with expected_outputs/ex2_2_expected.png

## Slide 8
Day 1 Capstone — Automated Frequency Response Tester
Team project • 105 minutes • the bridge to Multi-Instrument Mode
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Waveform Generator
sine sweep
20+ points, log-spaced
1
Loopback
Output 1 → Input 1
(later: a real DUT)
2
Oscilloscope
capture at each
frequency
3
Analysis & Report
gain in dB
Bode plot + CSV
4
Requirements
100 Hz – 10 MHz, 20+ log points
Gain = 20·log10(Vout/Vin)
CSV + Bode plot + short report
Evaluation
Functionality 40% • Code 20%
Documentation 20% • Results 20%
Checkpoints: 15 min — plan documented • 30 min — single measurement works • 60 min — full loop runs

## Slide 9
Capstone Presentations — Your Turn!
5 minutes per team, strictly timed
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
0:30
Problem statement
1
1:00
Approach &
instruments
2
2:00
LIVE DEMO
run the code
3
1:00
Challenges &
solutions
4
0:30
Q&A
5
✓
Live demo beats slides — show the script producing real data
✓
Tell us the one bug that cost you the most time, and how you found it
✓
Evaluation: Functionality 40% • Code 20% • Results 20% • Presentation 20%

## Slide 10
Multi-Instrument Mode (MiM)
The most powerful feature of the platform — two instruments, one device
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Traditional: One at a Time
Only ONE instrument loaded
Switch manually, lose state
Slow for stimulus-response tests
MiM: Two at Once
Slot 1 + Slot 2 run simultaneously
Internal digital routing — no cables
platform_id=2 on Moku:Go
# WRONG — plain dict: duplicate keys silently vanish
m.set_connections(connections={'Slot1OutA': 'Slot2InA'})
# RIGHT — LIST of DICTS (hardware-verified)
m.set_connections(connections=[
dict(source='Slot1OutA', destination='Output1'),
dict(source='Input1', destination='Slot2InA'),
])
Write it down: connections is a LIST of DICTS. This is the #1 MiM mistake.

## Slide 11
Routing Configurations — Signal Pathways
Moku:Go, platform_id=2
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Sources
Input1, Input2 (physical inputs)
Slot1OutA, Slot1OutB
Slot2OutA, Slot2OutB
Destinations
Output1, Output2 (physical outputs)
Slot1InA, Slot1InB
Slot2InA, Slot2InB
Loopback Test
Slot1OutA → Slot2InA
scope sees WG directly
DUT Testing
Slot1OutA → Output1
Input1 → Slot2InA
signal passes through your DUT
Dual Compare
Slot1OutA → Slot2InA (generated)
Input1 → Slot2InB (external)

## Slide 12
MiM — Critical Rules
Hardware-verified — these are exam questions for the rest of the week
Day 2: Foundations — Part 2
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
DO
One MultiInstrument() connection
platform_id=2 for Moku:Go
connections = list of dicts
m.relinquish_ownership() in finally
settle ≥ 50 ms before capture
DON'T
Open separate instrument connections
Pass a plain dict to set_connections
Use set_trigger source='Input1' in MiM —
NOT valid; auto-trigger works
Release wg/osc individually — crashes

## Slide 13
Day 2 Complete!
What You Achieved Today
✓
Controlled the AWG — custom waveforms from numpy (lut_data)
✓
Controlled the Logic Analyzer — verified pattern-generator API
✓
Built and presented the Frequency Response Tester capstone
✓
Learned MiM: slots, routing, the list-of-dicts rule
✓
Know the 3 critical MiM rules by heart
Tomorrow — Day 3 Preview
▸ MiM hands-on: AM modulation
▸ Filter characterization (real RC)
▸ Real-time Datalogger streaming
▸ FFT, SNR & THD analysis
▸ Day 2 Capstone begins
Homework
1. Finish your frequency response tester refinements
2. Read the workbook pages on MiM and streaming
3. Bring an RC filter idea for tomorrow
Spruha Build-in Solutions | Powered by Moku:Go — Liquid Instruments