## Slide 1
DAY 3 OF 5
Integration & Advanced Techniques
"Building Complex Test Systems"
5-Day SDI Lab Automation FDP • v2.0
Mahaveer. Rajendra. Savanur
Head of Engineering & AI Systems
Spruha Build-in Solutions | Powered by Moku:Go — Liquid Instruments

## Slide 2
Day 3 Agenda
Day 3: Integration & Advanced
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
1
8:00 – 9:00
Exercise 2.3: MiM Frequency Sweep WG + Oscilloscope, Bode plot
2
9:15 – 10:30
AM Modulation & Filter Characterization MiM hands-on
3
10:45 – 12:15
Real-Time Data Streaming Datalogger + Exercise 3.1
4
1:15 – 3:15
Advanced Analysis: FFT, SNR, THD Exercise 3.2 + signal quality
5
3:30 – 5:00
Day 2 Capstone Development team project time

## Slide 3
Exercise 2.3 — MiM Frequency Sweep
Day 3: Integration & Advanced
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
day2/ex2_3_mim_frequency_sweep.py
m = MultiInstrument(MOKU_IP, platform_id=2,
force_connect=True)
try:
wg = m.set_instrument(1, WaveformGenerator)
osc = m.set_instrument(2, Oscilloscope)
m.set_connections(connections=[
dict(source='Slot1OutA',
destination='Output1'),
dict(source='Input1',
destination='Slot2InA'),
])
# auto-trigger: 'Input1' is NOT a valid
# trigger source inside MiM
for freq in np.logspace(1, 5, 25):
wg.generate_waveform(channel=1, type='Sine',
amplitude=1.0,
frequency=freq)
osc.set_timebase(-5/freq, 5/freq)
time.sleep(0.3)
ch1 = osc.get_data()['ch1']
vpp = max(ch1) - min(ch1)
finally:
m.relinquish_ownership() # on m — ALWAYS
Hardware-verified March 2026 • deliverables: mim_sweep_data.csv + mim_sweep_bode.png
Key Concepts
Loopback check
flat ~0 dB across the sweep,
then insert an RC filter and
watch the cutoff appear
Timebase trick
±5 periods at every frequency:
set_timebase(-5/f, 5/f)
-3 dB cutoff
first point where Vpp drops
below 70.7% of reference

## Slide 4
MiM Hands-On — AM Modulation System
45 minutes • carrier + message in one box
Day 3: Integration & Advanced
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Slot 1: WG
100 kHz carrier
AM: 1 kHz message,
depth 50%
1
Internal Routing
Slot1OutA
→ Slot2InA
2
Slot 2: Scope
±2.5 ms window
5 modulation cycles
3
Analysis
envelope (hilbert)
measured depth ≈ 50%
4
✓
wg.set_modulation(channel=1, type='Amplitude', source='Internal', frequency=1e3, depth=50)
✓
Verify: ~100 carrier cycles per modulation cycle, smooth 1 kHz envelope
✓
Depth from data: (Vmax − Vmin) / (Vmax + Vmin) × 100% — expect 50% ± 5%
✓
Bonus: try depths 25 / 75 / 100%, vary the message frequency

## Slide 5
MiM Hands-On — Filter Characterization
Day 3: Integration & Advanced
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Objective: Characterize a real RC low-pass filter: Bode plot, cutoff, roll-off — the measurement every circuits lab needs
Requirements
✓
Loopback sanity first: flat ≈ 0 dB
✓
Insert RC filter: Out1 → R → C → In1
✓
Sweep 10 Hz – 100 kHz, log-spaced
✓
Gain (dB) = 20·log10(Vout/Vin)
✓
Find the −3 dB cutoff frequency
✓
Compare with theory: fc = 1/(2πRC)
Expected Output
[12/25] 158.5 Hz: 0.99 V (-0.1 dB)
[18/25] 2511.9 Hz: 0.71 V (-3.0 dB)
<-- cutoff region
[25/25] 100000 Hz: 0.06 V (-24.4 dB)
-3dB cutoff: ~2512 Hz
Theory 1/(2*pi*RC): 2653 Hz
Duration: 45 minutes | pairs
Bonus Challenge: Quality factor Q, roll-off rate in dB/decade, theoretical curve overlay

## Slide 6
Multi-Instrument Mode — Best Practices
Day 3: Integration & Advanced
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Connection
Single MultiInstrument() manages all
platform_id=2 for Moku:Go
Check set_connections() result
Timing
Wait ≥ 50 ms after frequency change
SETTLE_TIME in config.py
Longer settle for low frequencies
Cleanup
try / finally around everything
m.relinquish_ownership() — on m only
Never on the slot instruments
Frontend in MiM
Use m.set_frontend(...) on the
MultiInstrument object, not the
individual instruments

## Slide 7
Real-Time Streaming — Live Demo
Day 3: Integration & Advanced
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
day3/ex3_1_datalogger_streaming.py
from moku.instruments import Datalogger
dl = Datalogger(MOKU_IP, force_connect=True)
try:
dl.set_frontend(channel=1, impedance='1MOhm',
coupling='DC', range='10Vpp')
dl.generate_waveform(1, 'Sine', frequency=100)
dl.enable_input(2, enable=False)
dl.start_streaming(duration=10,
sample_rate=10e3)
while True:
try:
data = dl.get_stream_data()
if data:
ch1 = data['ch1']
print(len(ch1), 'samples,',
f'Vpp={max(ch1)-min(ch1):.4f}V')
except Exception as e:
if 'End of stream' in str(e):
break # NORMAL completion
raise
finally:
dl.relinquish_ownership()
Snapshot (get_data) = one frame • streaming = continuous flow, chunk by chunk
Key Concepts
'End of stream'
is EXPECTED at the end of a
fixed-duration stream —
catch it, do not treat as error
Use cases
long-term monitoring, burn-in,
live dashboards, 24/7 logging
Buffering
deque(maxlen=N) keeps the
last N samples for live plots

## Slide 8
Exercise 3.1: Streaming Monitor
Day 3: Integration & Advanced
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Objective: Stream real-time voltage data with live statistics and save every sample to CSV
Requirements
✓
Stream 10 s at 10 kSa/s, Input 1 only
✓
100 Hz test sine via BNC loopback
✓
Per chunk: count, mean, std, Vpp — live
✓
Catch 'End of stream' to exit cleanly
✓
Save ~100,000 samples to stream_data.csv
✓
Print the final summary statistics
Expected Output
Chunk 1 | 1024 | 0.0001 | 0.3527
Chunk 2 | 1024 | -0.0002 | 0.3531
...
Stream complete!
Total samples: 100,000
Data saved: stream_data.csv
Duration: 30 minutes
Bonus Challenge: Convert volts to "temperature" (T = V × 20) and alert above 80 °C; add a moving average
Script: day3/ex3_1_datalogger_streaming.py

## Slide 9
FFT, SNR & THD — Implementation
Day 3: Integration & Advanced
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
day3/ex3_2_fft_snr_thd.py
data = osc.get_data()
ch1 = np.array(data['ch1']) # lists -> arrays
t = np.array(data['time'])
N, dt = len(ch1), t[1] - t[0]
window = np.hanning(N)
fft_mag = 2.0/N * np.abs(np.fft.rfft(ch1*window))
freqs = np.fft.rfftfreq(N, dt)
# dominant frequency (skip DC bin)
peak = np.argmax(fft_mag[1:]) + 1
# SNR: peak power vs everything else
sig = fft_mag[peak]**2
noise = np.mean([fft_mag[i]**2
for i in range(1, len(fft_mag))
if abs(i - peak) > 2])
snr_db = 10*np.log10(sig / max(noise, 1e-20))
# THD: harmonics 2..5 vs fundamental
h = [fft_mag[peak*k] for k in range(2, 6)
if peak*k < len(fft_mag)]
thd = np.sqrt(sum(x**2 for x in h)) / fft_mag[peak]
Convert lists to arrays FIRST — get_data() returns Python lists
Key Concepts
Benchmarks
SNR > 40 dB: clean signal
THD < 1%: pure tone
how does yours compare?
Hann window
reduces spectral leakage on
non-integer cycle captures
Grading
GOOD / FAIR / POOR thresholds
printed by the script

## Slide 10
Exercise 3.2: Signal Quality Report
Day 3: Integration & Advanced
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Objective: Capture a frame, compute its FFT, and grade the signal with SNR and THD
Requirements
✓
Capture: 1 kHz sine, 0.5 Vpp, loopback
✓
np.array() conversion before FFT
✓
Find dominant frequency vs expected
✓
SNR with GOOD/FAIR/POOR grade
✓
THD over harmonics 2–5 with grade
✓
4-panel plot: time, FFT, harmonics, report
Expected Output
Captured: 1024 samples at 102.4 kSa/s
Dominant frequency: 1000.0 Hz
SNR: 58.3 dB (GOOD)
THD: 0.41 % (GOOD)
Plot: fft_snr_thd_analysis.png
Duration: 45 minutes
Bonus Challenge: Where does the noise come from? What would clipping do to THD? Try amplitude 2.5 V and see.
Script: day3/ex3_2_fft_snr_thd.py • compare with expected_outputs/ex3_2_expected.png

## Slide 11
Day 2 Capstone — Professional Test System
Starts now, presents tomorrow morning
Day 3: Integration & Advanced
5-Day SDI Lab Automation FDP • v2.0
Powered by Moku:Go — Liquid Instruments
Multi-Instrument Mode
WG + Scope
internal routing
1
Parametric Sweep
frequency loop
gain at each point
2
Quality Metrics
FFT / SNR / THD
from Exercise 3.2
3
Professional Output
CSV + plots
written report
4
✓
Combine everything from Days 1–3 into one coherent, automated system
✓
Homework tonight: finish the system, prepare a 5-minute presentation
✓
Presentations tomorrow 8:20 AM — live demo required

## Slide 12
Day 3 Complete!
What You Achieved Today
✓
Ran two instruments simultaneously with MiM routing
✓
Built AM modulation and characterized a real RC filter
✓
Streamed real-time data, handled End-of-stream correctly
✓
Measured signal quality: FFT, SNR, THD with numpy
✓
Started the Day 2 capstone — the professional test system
Tomorrow — Day 4 Preview
▸ Capstone presentations
▸ Industry case studies
▸ The 5 automation patterns
▸ Final capstone: A / B / C
▸ Awards & Day 5 preview
Homework
1. Finish the Day 2 capstone system
2. Prepare a 5-minute presentation with live demo
3. Review Days 1–3 API patterns
Spruha Build-in Solutions | Powered by Moku:Go — Liquid Instruments